## Slide 1
CLASSIFICATION OF RIVERS AND LAKES
IN ESTONIA
Peeter Marksoo
CIS WORKSHOP ON NATIONAL CLASSIFICATION SYSTEMS FOR THE ASSESSMENT OF THE ECOLOGICAL STATUS OF SURFACE WATERS
Paris, 11-12 June 2007

## Slide 2: The aim of the presentation
To give an overview about Estonian classification system for rivers and lakes
To get possible feedback and suggestions to improve our classification system

## Slide 3: Estonia belongs to Central /Baltic GIG
Area 43 432 km2
Population
1, 34 million
Population density
31 persons per km2

## Slide 4: Estonian classification system
was compiled during second half of 2006
and slightly modified this year taking into consideration the results of intercalibration in ECOSTAT
It is decided to test it this year and make corrections, if needed, next year

## Slide 5: General principles of surface water status assessment
The assessment of the status of a water body shall be based on monitoring data.
In absence of monitoring data, assessment can be based on an expert judgement, taking into account reference conditions, pressures, general impression of a water body.
The assessment can be also based on modelling.
In case of contradictions between physicochemical and biological quality indicators, the final status assessment can be based on expert judgement.
Water bodies of the same type and similar pressure can be grouped and the status assessment based on comparison.
In case there is no evidence of pressure and impact, the status assessment can be based on expert judgement.

## Slide 6: Estonian lakes
There are more than 1200 lakes (>1 ha) in Estonia
Two large lakes, Lake Peipsi and Lake Võrtsjärv
Estonian lakes have been investigated for more than 100 years
Estonian Limnologists Society celebrated its centennial in 2005.
Therefore Estonian lake typology is relatively well elaborated.
Present typology for purposes of WFD is derived from more detailed and sophisticated former typologies.

## Slide 7
Lake
Peipsi
Lake Võrtsjärv

## Slide 8: Estonian lake types
type I – calcareous lakes (alkalinity >240 HCO3 mg/l, conductivity >400 µS/cm);
type II – shallow lakes with medium water hardness (unstratified, alkalinity 80–240 HCO3 mg/l, conductivity 165-400 µS/cm);
type III – deep lakes with medium water hardness (stratified, alkalinity 80–240 HCO3 mg/l, conductivity 165-400 µS/cm);
type IV – softwater (alkalinity <80 HCO3 mg/l, conductivity <165 µS/cm) dark coloured lakes (absorbance factor at 400 nm >4 m-1, colour >8);
type V – softwater (alkalinity <80 HCO3 mg/l, conductivity <165 µS/cm) light coloured lakes (absorbance factor at 400 nm ≤ 4 m-1, colour ≤ 8);
type VI – Lake Võrtsjärv – medium hardness (unstratified) shallow light coloured lake (absorbance factor at 400 nm ≤ 4 m-1, colour ≤ 8);
type VII – Lake Peipsi – medium hardness (unstratified) shallow light coloured lake (absorbance factor at 400 nm ≤ 4 m-1, colour ≤ 8);
type VIII – coastal lakes (distance from the sea <5 km) – medium depth (< 1m) light coloured lakes (absorbance factor at 400 nm ≤ 4 m-1, colour ≤ 8), content of chlorines >25 mg/l).

## Slide 9: Assessment of the ecological status of lakes
Biological quality elements are:
composition, abundance and biomass of phytoplankton;
composition and abundance of macrovegetation;
composition and abundance of benthic invertebrate fauna.
Chemical and physicochemical quality elements are:
transparency,
range of metalimnion,
acidification status and
nutrient conditions.

## Slide 10: Type II: shallow lakes with medium hardness water Chemical and physicochemical quality elements
Indi-cator | Unit | High | Good | Moderate | Poor | Bad
pH |  | 7-8,5 | 7-8,0 | <7 or >8,5 | <7 or >8,5 | <7 or >8,5
Total P | micro-grams/l | <30 | 30-60 | >60-80 | >80-100 | >100
Total N | micro-grams/l | <500 | 500-700 | >700-1000 | >1000-1300 | >1300
Secchi depth | m | >3 | 2-3 | 1-<2 | <1 | <1

## Slide 11: Type II: shallow lakes with medium hardness water Biological quality elements
Plant community - More important taxa by turns of abundance
Potamogeton perfoliatus and/or P.lucens, relative abundance - Braun-Blanquet scale (0–5)
Charophyta and/or Bryophyta, relative abundance - Braun-Blanquet scale (0–5)
Ceratophyllids and/or lemnids, relative abundance - Braun-Blanquet scale (0–5)
Large green philamentous algae, abundance - abundance scale 0–5 related to abundance of other hydrophytes
Chlorophyll a content of the water column - micrograms/l
Surface layer (0.5m) Chlorophyll a content - micrograms/l
Phytoplankton community
Phytoplankton compound quotient

## Slide 12
Macroinvertebrates :
- Number of taxa
- Number of sensitive taxa (EPT)
- Shannon diversity index
- Mean sensitivity of taxon (ASPT)
- Acidity index (A)

## Slide 13: The ecological status assessment of a lake is based on quality indicators, not on quality elements
From each quality element (biological, hydromorphological and physicochemical) at least one quality indicator shall be represented.
At least seven quality indicators shall be used and all indicators are of equal relative importance.
The final assessment is based on 2/3 of indicators.
It means that some indicators (up to 1/3 of total number of used indicators) can exert lower value than that in the final assessment.

## Slide 14: Hydromorphological quality indicators
changes of water level,
status of the protection zone,
structure of the lake shore and
lake depth variation.
The final assessment of hydromorphological status is given as expert judgement.

## Slide 15: Lake Viljandi

## Slide 16: Lake Uljaste

## Slide 17
Lake Viljandi
type III - deep stratified lakes with medium water hardness
Total status – good
Lake Uljaste
type V - softwater light coloured lakes
Total status - moderate
Q. Element | Unit | Lake Uljaste | Lake Viljandi
Total P | mg/l | 0,016 | 0,031
Total N | mg/l | 0,4 | 1,2
Secchi depth | m | 2,5 | 1,4
pH |  | 8,2 | 8,3
Chl a, surface | µg/l | 6,7 | 14,4
Chl a, water coloumn | µg/l |  | 12,2
Phytoplankton compound quotient |  | 4,5 | 4,3
Phytoplankton community |  |  | 
Macro-inverte-brates | Shannon DI | 2,66 | 2,41
 | ASPT | 6,08 | 5,30
 | EPT | 7 | 7
 | Aciditi I | 3 | 7
 | No of taxa | 16 | 24

## Slide 18: Estonian Rivers
7274 rivers 10 – 25 km long
98 rivers 25-100 km
6 rivers > 100 km
The only large river in European concept is River Narva (catchment area 56 200 km2)
Rivers in Estonia have been investigated mainly from hydrological and hydrochemical viewpoint.
More systematic studies of biota of Estonian rivers started only during 1990ies.
There was no river typology suitable for purposes of WFD before.
Present typology should be dealt as preliminary version
In particular the boundary between darkwater humic rivers and lightwater rivers should be checked and possibly shifted toward more humic side.

## Slide 19: Estonian river types
type I A – darkwater and humic rivers (CODMn 90th percentile value over 25 mgO/l) with catchment area 10– 100 km2;
type I B – lightwater and low organic content (CODMn 90 percentile value under 25 mgO/l) rivers with catchment area 10–100 km2;
type II A – darkwater and humic rivers with catchment area 100–1000 km2;
type II B – lightwater rivers, catchment area 100 -1000 km2;
type III A – darkwater and humic rivers, catchment area 1000–10 000 km2;
type III B – lightwater rivers, catchment area 1000 – 10000 km2;
type IV – rivers with catchment area over 10 000 km2.

## Slide 20: Biological quality elements used in Estonian river classification
Phytobenthos, three diatoms indexes, which are indifferent for the river type and show mainly water quality:
IPS - Specific Polluosensitivity Index
WAT – Watanabe index
TDI – Trophic Diatom Index
The samples shall be taken in summer during low-water period.
The assembled status assessment is given as arithmetic mean of three indexes.

## Slide 21: Phytobenthos, class boundaries
The same boundaries for all river types
Index | High | Good | Moderate | Poor | Bad
IPS | >15,5 | 15,5>12,0 | 12,0–>9,5 | 9,5–6,9 | <6,9
WAT | >15 | 15,9–>12,4 | 12,4–>9,7 | 9,7–7,1 | <7,1
TDI | <75 | 75–<80 | 80–<85 | 85–<90 | 90–100

## Slide 22: Macroinvertebrates River types 1A and 1 B
Indicator | High | Good | Moderate | Poor | Bad
Number of taxa | >26 (rhithral) >16 (potamal) | 26-23 (r) 16-14 (p) | 22-17 (r) 13-11 (p) | <17 (r) <11 (p) | <17 (r) <11 (p)
Number of sensitive taxa (EPT) | >12 (rhithral) >8 (potamal) | 12-10 (r) 8-7 (p) | 9-8 (r) 6-5 (p) | <8 (r) <5 (p) | <8 (r) <5 (p)
Shannon diversity index | >2,1(lime-stone bedrock) > 2,7 (sand-stone bedrock) | 2,1-1,9 (lim) 2,7-2,4 (sand) | <1,9-1,4 (lim) <2,4-1,8 (sand) | <1,4 (lim) <1,8 (sand) | <1,4 (lim) <1,8 (sand)
ASPT | >5,9 (rhithral) >5,5 (potamal) | 5,9-5,3 (r) 5,5-4.9 (p) | 5,3-4 (r) 4,9-3,7 (p) | <4 (r) <3,7 (p) | <4 (r) <3,7 (p)
DSFI | 7-6 | 5 | 4 | <4 | <4

## Slide 23: Macroinvertebrates
The macroinvertebrates classification for rivers can be applied if the samples are taken in April-May and/or September/November.
The assembled status assessment is given on the basis of five macroinvertebrates indexes.

## Slide 24: Fish
Type-specific species – all species in a river section except „occasional visitors“. The river section is for these species a habitat, spawning ground or migration route.
Indicator species – typical species for the river section, which occurrence and status have a priority importance in assessment the status of the river section.
An age structure of indicator species is assessed in the following age groups: 0+ (one summer old); 1+ (two summer old); older specimen >1+
Prerequisite for assessment is the existence of suitable habitats for age groups and occurrence of age groups is anticipated consequently from life-cycle of the species.
Type-specific and indicator species are determined separately for each river type. The determination is based on fish typology of rivers, where the rivers are divided into sub-types taking into account fish’s requirements for habitats and living conditions.
In certain cases, when a species is absent because of natural reasons, an expert can make changes in the list of type-specific and indicator species

## Slide 25: Fish
For all river types
Indicator | Unit | High | Good | Moderate | Poor | Bad
Indicator species | % | 100 | <100–80 | <80–50 | <50–20 | <20
Type-specific species | % | 100–80 | <80–60 | <60–40 | <40–20 | <20
Age structure of indicator species | % of species with three age groups | 80 | <80-60 | <60-40 | <50-20 | <20
 | % of species with two age groups | 100 | <100-80 | <80-50 | <50-20 | <20

## Slide 26: Hydromorphological quality indicators
longitudinal and lateral continuity of the river,
river depth and width variation, river slope and river width,
structure and substrate of the river bed,
quantity and dynamics of water flow in low-water period and during the year,
structure and extent of the riparian zone,
existence of flood plain.
The final assessment of hydromorphological status is given as expert judgement.

## Slide 27: Chemical and physicochemical quality elements
Lightwater rivers with low humic substances content, Types 1B, 2B and 3B
Indicator | Unit | High | Good | Moderate | Poor | Bad
O2, | Saturation %, 10 percentile | >70 | 70-60 | <60-50 | <50-40 | <40
BOD5 | mgO2/l (75%) | <2,5 | 2,5-4,0 | 4,1-6,0 | 6,1-8,0 | >8,0
Total N | mgN/l (75%) | <1,5 | 1,5-2,4 | 2,5-3,1 | 3,2-3,9 | >3,9
Total P | mgP/l (75%) | <0,04 | 0,04-0,06 | >0,06-0,08 | >0,08-0,11 | >0,11
pH |  | 6-9 | 6-9 | 6-9 | 6-9 | <6 or >9

## Slide 28
River Väike-Emajõgi
Macroinvertebrates indexes
1996
2001
2006

## Slide 29: River Väike Emajõgi Phytobenthos, three diatoms indexes,

## Slide 30: River Väike Emajõgi Water quality (mean values, mg/l)

## Slide 31
River Pärnu
Macroinvertebrates indexes
1996
2001
2006

## Slide 32: River Pärnu Phytobenthos, three diatoms indexes,

## Slide 33: River Pärnu Water quality (mean values, mg/l)

## Slide 34: Main problems encountered during the compilation of the classification
Estonia is a small country and main attention of monitoring has been given to larger rivers. Therefore it is difficult to compile good database on reference water bodies.
The number of monitored lakes and rivers is not very high, because financial and also human resources are limited.
Sampling sites for biological and hydrochemical monitoring of rivers have been different in former times – therefore there were difficulties in comparing class boundaries for biological and chemical quality elements.

## Slide 35: Main problems encountered during the compilation of the classification
The water quality of Estonian rivers has improved during last 15 years
Hydromorphological monitoring for rivers will start only this year
Today hydromorphological factors (dams, land reclamation, draining) have often more impact on biological quality elements than water quality has.
In conditions of changing water quality and scarce hydromorphological data → difficult to find out reasons for lower than good biological quality.
Accidental pollution (for example manure was spread on snow) can have considerable impact on biota, but not recorded in chemical monitoring → difficult to find out reasons for lower than good biological quality.