## Slide 1: EFFECT OF AGGREGATION METHODS ON ECOLOGICAL ASSESSMENT
Paul Latour
Ministry of Transport, Public Works and Water Management
CIS WORKSHOP ON NATIONAL CLASSIFICATION SYSTEMS FOR THE ASSESSMENT OF THE ECOLOGICAL STATUS OF SURFACE WATERS
Paris, 11-12 June 2007

## Slide 2
INFORMATION
NEEDS
MONITORING STRATEGY AND DESIGN
DATA COLLECTION/
STORAGE
DATA ANALYSIS
INFORMATION
UTILISATION AND REPORTING
WATER MANAGEMENT
WFD
WFD-format
Annual water quality questionnaire
Database-structures
AQUO data standardized format
Monitoring programs, guidelines
Assessment systems
Annual report to Parliament
WFD reporting
Regional and thematic reports
WFD-geo portal
THE MONITORING CYCLE
National water policy
Notes: The cycle descibes the proces from specifying information needs and a monitoring strategy to collecting information through sampling and data-analysis up to utilisatioon of resulting information. The cycle was developed in the preparation of the Guidelines on water quality monitoring and assessment of transboundary rivers bij the UN/ECE Task Force on Monitoring and Assessment in 1996.

## Slide 3: Data analysis, assessment and reporting
Standard format for data storage / data exchange
Harmonised metrics / objectives (e.g. intercalibration)
Standard assessment tools
Harmonisation of calculation methods in ‘preprocessing’ of monitoring data ?
Does aggregation method influence
assessment result?

## Slide 4: Examples of how indicative parameters may be combined to estimate the condition of the biological elements
Averaging:
how and what ?

## Slide 5: Temporal aggregation of monitoring data
year | month | value
2000 | Jan | 
 | Febr | 
 | March | 
 | ¦ | 
 | ¦ | 
 | Oct | 
 | Nov | 
 | Dec | 
2001 | Jan | 
 | Febr | 
 | March | 
 | ¦ | 
 | ¦ | 
 | Oct | 
 | Nov | 
 | Dec | 
2002 | Jan | 
 | Febr | 
 | March | 
 | ¦ | 
 | ¦ | 
 | Oct | 
 | Nov | 
 | Dec | 
 |  | AVERAGE
 | 2000 | 2001 | 2002 | 
Jan |  |  |  | monthly average
Febr |  |  |  | monthly average
Mar |  |  |  | monthly average
Apr |  |  |  | monthly average
May |  |  |  | monthly average
June |  |  |  | monthly average
July |  |  |  | monthly average
Aug |  |  |  | monthly average
Sept |  |  |  | monthly average
Oct |  |  |  | monthly average
Nov |  |  |  | monthly average
Dec |  |  |  | monthly average
 | annual average | annual average | annual average | AVERAGE

## Slide 6: Spatial aggregation of monitoring data
(sub)sites within subbasin
º representative (WFD) site for a basin

## Slide 7: Scenarios for aggregation
Temporal aggregation in two ( ) or one ( ) calculation(s)
Spatial aggregation: two alternatives ( )
Temporal and spatial aggregation in different order

## Slide 8: First temporal aggregation, then spatial (physico-chemistry)
Table with monitoring data of one site
Column = year
Row = month
water body
(sub) basin

## Slide 9: First spatial aggregation, then temporal (physico- chemistry)
Table with monitoring data, average values of several sites
Table combining monitoring data of several sites

## Slide 10: Temporal and spatial aggregation in one step (physico-chemistry)
9 out of 20 possibilities in case study

## Slide 11: Water bodies in province of Flevoland
Water body types: mainly small canals and very shallow lakes

## Slide 12: Monitoring sites WFD
WFD-sites assumed to be representative for underlying monitoring network

## Slide 13: Results from 9 scenario’s for aggregating physico-chemical data
 | COPPER (ug/l) |  | 
Scenario | WFD-site 00532 | WFD-site 00524 | WFD-site BUV95
1 | 1.53 | 1.29 | 1.75
2 | 1.63 | 1.36 | 1.82
3 | 1.53 | 1.29 | 1.75
4 | 1.60 | 1.76 | 2.02
5 | 1.74 | 1.87 | 2.02
6 | 1.59 | 1.56 | 1.79
7 | 2.02 | 2.00 | 1.94
8 | 1.74 | 1.69 | 1.83
9 | 1.67 | 1.61 | 1.86
minimum | 1.53 | 1.29 | 1.75
maximum | 2.02 | 2.00 | 2.02
deviation | 0.49 | 0.71 | 0.27
average | 1.67 | 1.60 | 1.86
PHOSPHATE (mg/l) |  | 
WFD-site 00532 | WFD-site 00524 | WFD-site BUV95
0.23 | 0.19 | 0.19
0.24 | 0.15 | 0.18
0.23 | 0.19 | 0.19
0.22 | 0.16 | 0.17
0.26 | 0.18 | 0.16
0.22 | 0.16 | 0.16
0.16 | 0.12 | 0.13
0.22 | 0.15 | 0.16
0.22 | 0.15 | 0.16
0.16 | 0.12 | 0.13
0.26 | 0.19 | 0.19
0.10 | 0.07 | 0.16
0.22 | 0.16 | 0.17
Objectives:
Copper: 1.5 ug/l
Phosphate: 0.15 mgP/l
No conclusion possible which scenario is best
Data not equally distributed over sites and years
Compliance depending on aggregation method !

## Slide 14: Consequence of unequal data-distibution: Effect of variation in time of monitoring results
 | Site A | Site B | average | 
Jan | 9 |  | 9.0 | 
Febr | 8 |  | 8.0 | 
Mar | 6 |  | 6.0 | 
Apr | 4 | 1 | 2.5 | 
May | 1 | 1 | 1.0 | 
June | 0 | 0 | 0.0 | 
July | 1 | 2 | 1.5 | 
Aug | 2 | 2 | 2.0 | 
Sept | 3 |  | 3.0 | 
Oct | 6 |  | 6.0 | 
Nov | 8 |  | 8.0 | 
Dec | 9 |  | 9.0 | 
 | 4.8 | 1.2 |  | 4.7
 |  |  | 3.0 | 
If variation in time of data is high: spatial aggregation first
Site B: little data in period with high concentrations

## Slide 15: Consequence of unequal data-distibution: Effect of spatial variation in monitoring results
 | Site A | Site B | average | 
Jan | 3 |  | 3.0 | 
Febr | 4 |  | 4.0 | 
Mar | 3 |  | 3.0 | 
Apr | 3 | 8 | 5.5 | 
May | 4 | 9 | 6.5 | 
June | 5 | 9 | 7.0 | 
July | 4 | 8 | 6.0 | 
Aug | 3 | 8 | 5.5 | 
Sept | 3 |  | 3.0 | 
Oct | 4 |  | 4.0 | 
Nov | 3 |  | 3.0 | 
Dec | 3 |  | 3.0 | 
 | 3.5 | 8.4 |  | 4.5
 |  |  | 6.0 | 
If spatial variation of data is high: temporal aggregation first
less data from site with
higher concentrations

## Slide 16: Calculate EQR first, then temporal and/or spatial aggregation (biology)
Table with monitoring data of one site
Column = year
Row = species
water body
(sub) basin

## Slide 17: Temporal or spatial combination of data, then calculate EQR (biology)
Table with combined / aggregated species list
Column = year
Row = species
Combined / aggregated species list for several years (‘temporal aggegation’)

## Slide 18: Results from 5 scenario’s for aggregating biological data
Scenario | Large ditches (tochten) | Small canals (vaarten) | Lakes
Macrophytes EQR |  |  | 
1 | 0.014 | 0.067 | 0.059
2 | 0.013 | 0.078 | -
3 | 0.136 | 0.077 | 0.039
4 | 0.478 | 0.293 | 0.038
5 | 0.573 | 0.203 | -
Macro-invertebrates EQR |  |  | 
1 | 0.420 | 0.366 | 0.390
2 | 0.415 | 0.356 | 0.390
3 | 0.419 | 0.366 | 0.390
4 | 0.504 | 0.416 | 0.390
5 | 0.520 | 0.414 | 0.390
Dutch metric for assessing macrophytes: at the level of water body (scenario 1,2 and 3 not permitted)
Dutch metric for assessing macro-invertebrates is validated according to scenario 1/2/3 (EQR at site level)
Notes: PS Though Dutch metrics for assessing macrophytes is at water body level, the intercalibration has been done assessing biological data at site level (also for Dutch sites !)

## Slide 19: Conclusion
If monitoring frequency at all sites is similar: no difference in order of aggregation (temporal/spatial)
If temporal variation of data is high: spatial aggregation first (e.g. phosphate, phytoplankton)
If spatial variation of data is high: temporal aggregation first (e.g. copper)
Biological quality elements: summing up lists of species per site before calculating EQR highly influences outcome of assessment (but: may differ per national metric)
Notes: Phosphate: calculate monthly averages first for all sites within a water body all together
Copper: calculate annual average per site, then aggregate sites
This presentation was not for showing you the best way for aggregating data, but to raise awareness that preprocessing does influence your assessment.