## Slide 1: General chemical and physico-chemical elements – Type-specific assessment of rivers in Austria
Karin Deutsch
BMLFUW VII 1
karin.deutsch@lebensministerium.at

## Slide 2: Introduction/1
WFD Annex V – Quality elements for the classification of ecological status
     Biological elements
    Hydromorphological elements
    Chemical and physico-chemical elements supporting the biological elements
        General
        Thermal conditions
        Oxygen conditions
        Salinity
        Acidification status
        Nutrient conditions
        Specific pollutants

## Slide 3: Introduction/2
WFD Annex V Tab. 1.2.1. Normative definitions Physico-chemical quality elements General conditions
High status: … elements correspond totally or near totally to undisturbed conditions
Good status: … range established to ensure functioning of the type specific ecosystem
… ensure achievment of the values specified for the biological quality elements
Ecological Classification Guidance (ECOSTAT 11/2003)

## Slide 4: General approach
Formulation of quality standards based on
existing monitoring data
WFD typology
assessment of biological quality elements with WFD compliant methods
 Makroinvertebrates – saprobic index as indicator for organic pollution
 Phytobenthos – trophic index as indicator for nutrient pollution
 Fish
Project:
Norbert Kreuzinger
Institute for Water Quality, Resources and Waste Management
Technical University Vienna
Notes: Based on the assessmentt of the biological quality elements the monitoringsites were selected – as an indicator for undisturbed conditions with organic and nutrient pollution monitoring sites with saprobic index border high to good and border good

## Slide 5
6 Ecoregions
abiotische Typisierung
Biological revision
15 bioregions
with further differentiation
SI / TI / fish
WFD Annex II - Typology
Notes: The future work will be to define some biologically based Regions.

## Slide 6: Typology Macroinvertebrates Saprobic index – reference condition

## Slide 7: Saprobic index high/good

## Slide 8: Typology Phytobenthos Trophic index – reference condition

## Slide 9: Trophic index high/good

## Slide 10: Data base
Monitoring data of 240 monitoring sites including reference sites for high and good status
2003 – 2005
Makroinvertebrate, Phytobenthos
Chemistry monthly

## Slide 11: Physico chemical quality elements – selection of parameters
General chemical and physico-chemical element | Parameter | High/good based on
Oxygenation conditions | BOD5, (Oxygen saturation) | Macroinvertebrate – Saprobic index
Nutrient conditions | NO3-N | Macroinvertebrate – Saprobic index
 | Soluble reactive phosphor | Phythobenthos – Trophic index
Salinity | Chlorid | Macroinvertebrate – Saprobic index, Fish
Acidification status | pH | Fish (CD 78/659/EEC)
 | (Acid Neutralising Capacity) | 
Thermal conditions | °C | Fish

## Slide 12: Oxygenation conditions – BOD5
General chemical and physico-chemical element | Parameter | High/good based on
Oxygenation conditions | BOD5 | Macroinvertebrate – Saprobic index
Data Processing
    Evaluation BOD/SI
    for each bioregion and high/good selection of monitoring sites which lie within the range boundary - 0,125 SI
     focus of the definition of boundary values

## Slide 13: Selection of relevant sites
Monitoring site | Bioregion | SI reference High/good | SI observed | Site used for standard determination
FW 39831200 | Südalpen | 1,5/2,03 | 1,8 | No – not within the range
FW 46996310 | Südalpen | 1,5/2,03 | 1,4 | Yes - high

## Slide 14: BOD – 90 percentile
BOD mg/l
Statistical data not available for all types

## Slide 15: Clusteranalysis
 Clusteranalysis identifies similar bioregions
 Expertjudgment

## Slide 16: BOD – Proposal quality standard
Proposal quality standard 2007 - values under discussion !
BOD/mg/l
Compliance checking-monthly data, 1 or 2years - 90 percentile

## Slide 17: Nutrients
General chemical and physico-chemical element | Parameter | High/good based on
Nutrient conditions | PO4-P (SRP) | Phytobenthos – Trophic index (TI)
 | NO3-N | Macroinvertebrate – Saprobic index
Data Processing
Phytobenthos - Trophic index - Definition high and good
for each bioregion selection of monitoring sites within the range boundary - 0,125 TI  focus of the definition of boundary values
exeption NO3-N: no nitrogen limitation in austrian rivers, high status  saprobic index
NH4-N, NO2-N – QS based on toxicology

## Slide 18: SRP or P(tot)
Why SRP?
Interrelation SRP – TI  high concentration strong indication for high TI  low concentrations don´t mean always low TI  Additional limitation factors – light?

## Slide 19: SRP – Proposal quality standard
Proposal quality standard 2007 -values under discussion!
SRP/mg/l
Compliance checking-monthly data, 1 or 2years - 90 percentile

## Slide 20: NO3-N Proposal quality standard
Proposal quality standard 2007 -values under discussion !
NO3-N/mg/l
Compliance checking-monthly data, 1 or 2years - 90 percentile
High status – values based on SI
Good status only differentation between si-reference no bioregion

## Slide 21: Salinity
High status based on saprobic index ??
Good status ??
General chemical and physico-chemical element | Parameter | High/good based on
Salinity | Chlorid | Macroinvertebrate – Saprobic index, Fish ?

## Slide 22: Acidification, Thermal conditions
Thermal condition – Temperature
  High status based on demands of typespecific fishpopulation
  Good status – Fish Protection Directive (CD 78/659/EEC)
  Qualitity standards - still open
General chemical and physico-chemical element | Parameter | High/good based on
Acidification status | pH | Fish (CD 78/659/EEC)
 | (Acid Neutralising Capacity) | 
Thermal conditions | °C | Fish
Acidification status – ph based on Fish Protection Directive (CD 78/659/EEC)

## Slide 23: Ecological status of monitoring site
Assessment of ecological status of monitoring sites requires biological and chemical data
General chemical and physico-chemical elements:
    Under discussion
    Compliance checking requires monthly data from 2 years
    90 percentile
    Every single parameter counts
Biological qualitiy elements
 Worst case

## Slide 24
Conformance TI - SRP | 
Algae = SRP | 38%
Algae | 54%
SRP | 8%

## Slide 25
Thank you for your attention
Thank you for your attention