## Slide 1: UK presentation - Session C Physicochemical results and combining results across quality elements
Our presentation will cover
  Uncertainty – why do we need to consider it ?
  Using information on Confidence
  Chemical quality, particularly nutrients
  Examples
  Checking Procedure

## Slide 2: Uncertainty as an issue in river basin management
10%
30%
40%
15%
5%
We can make an accurate estimate of numbers of water bodies in each class

## Slide 3: Uncertainty as an issue in river basin management
10%
30%
40%
15%
5%
But…..
Quite a lot of water bodies will be in the wrong class

## Slide 4: Uncertainty as an issue in river basin management
10%
30%
40%
15%
5%
Quite a lot of water bodies will be in the wrong class
And we won’t know which ones !

## Slide 5: We sample water bodies
Every estimate made from monitoring will have some error
You need to measure this

## Slide 6
High
Good
Moderate
Poor
Bad
100 % sure status is good

## Slide 7
High
Good
Moderate
Poor
Bad
100 % sure status is worse than good

## Slide 8
High
Good
Moderate
Poor
Bad
This is High Confidence
We can be certain this water body is worse than Good
This is Lower Confidence
We are much less certain that this water body is worse than Good
Both water bodies are Moderate, but

## Slide 9
Bad
Poor
High confidence moderate or worse
Moderate
Good
High
Confidence of class
Face value classification

## Slide 10
Bad
Poor
Less than high confidence moderate or worse
Moderate
Good
High
Confidence of class
Face value classification

## Slide 11
Information on confidence is important for:
Objective setting
Prioritising monitoring efforts
Notes: Confidence information is important for:
Objective setting
Prioritising monitoring efforts

## Slide 12
Less than high confidence
High confidence
Prioritise further monitoring & assessment
Control risk of deterioration
Delay expensive measures until confidence increased
Prioritise for improvement…
….depending on objective setting process

## Slide 13
100s of water bodies classed worse than good….
Face value classification basis for national or regional measures
…in relation to a particular pollutant or issue
…high confidence that there is a truly problem
basis for considering national or regional measures (e.g. product controls)

## Slide 14
..but information on confidence of class needed to prioritise targeted measures

## Slide 15
Combining results for certain physicochemical & biological quality elements

## Slide 16
Nutrients
Temperature
Set class boundary standards to support biology
Uncertainties about the correct value to set for the standards

## Slide 17
Uncertainty arises because of different ecological sensitivities in different water bodies
Typology reduces uncertainty but can’t remove it

## Slide 18
CO2
Nutrients
Plant biomass
Oxygen deficit
Oxygen deficit
Plant biomass
Nutrients

## Slide 19: Confidence after combining certain physicochemical & biological quality elements
..and use weight of evidence to improve our confidence of class
Take account of this uncertainty in the confidence of class we assign…

## Slide 20
Bad
Bad
Poor
Poor
Moderate
Moderate
Good
Good
High
High
Biological results
Nutrient results
Bad
Poor
Low confidence moderate
Moderate
Good
High
Confidence of class
Ecological class

## Slide 21
Bad
Bad
Poor
Poor
Moderate
Moderate
Good
Good
High
High
Biological results
Nutrient results
Bad
Poor
High confidence moderate
Moderate
Good
High
Confidence of class
Ecological class

## Slide 22: Case study A: Belfast Lough, Northern Ireland)
Nutrients fail
Chl a fails in ’90s
Macroalgae –nuisance blooms
Benthos - impacted
Management action & designation as SA
Reduction in chl a
Step changes in benthos
Notes: First example – we would like to take you to Belfast Lough in Northern Ireland, which is an example of a clear case of where class would have been less than good in the 90’s - although WFD tools were not then available, and where, by taking management action, we are now seeing real improvements. Belfast Lough is on the east coast of Northern Ireland and is a shallow, fully marine lough with the city of Belfast at its western end. Population of approximately 0.75 million live around its shores.
Click 1 – Nutrient concentrations very high – due primarily to poor sewage treatment and a fertilizers industry discharging into inner Lough
Click 2 – Very high chlorophyll levels
Click 3 – Accompanied by nuisance algal blooms, Alexandrium, PSP and clearly impacted benthic infauna
Click 4 – Total Loading of N to inner Lough. In late 90’s – early 00’s started to introduce secondary sewage treatment and then added N removal to Belfast’s 2 biggest sewage works. Late 2002 – industry closed (after much pressure to reduce its N loading to Lough). Also a designation was made under UWWTD. This designation was late, but the appropriate management action was taken.
Click 5 – DIN in Lough also reduced and we can see a big normalisation in chlorophyll concentrations
Click 6 – Over the period of greatest change, we saw a step change in the benthic invertebrates – heading towards good?
Obviously more data behind this example – but just a snap shot to let you see how things might work.

## Slide 23: Case Study A: Belfast Lough
Invertebrates
Macroalgae
Phytoplankton
Nitrogen
Bad
Poor
Mod
Good
High
Ecological status = ‘poor’ with high confidence
Follow up: measures to reduce nutrient inputs to the water body

## Slide 24: Case study B :(Lake in NW England) Confidence (%) of Class
 | High | Good | Mod | Poor | Bad
Phosphorus | 0 | 0 | 100 | 0 | 0
Phytoplankton | 0 | 40 | 60 | 0 | 0
Phytobenthos | 1 | 99 | 0 | 0 | 0
Macrophyte | 0 | 91 | 9 | 0 | 0
Invert | 0 | 99 | 1 | 0 | 0
Ecological status = ‘moderate’ with medium confidence
Follow up: prioritise for further monitoring and analysis; control risk of deterioration

## Slide 25: Case study C : Lake in Wales Confidence (%) of Class for
Ecological status = ‘moderate’ with low confidence
Follow up: continue to monitor; check data for trends; if such mismatches common for type, apply checking procedure

## Slide 26: Checking Procedure Section 4 of CIS classification guidance
Apply if mismatches are common in a type
If isolated mismatch, there may be a site specific sensitivity, or insufficient information to check standard

## Slide 27: Uncertainty as an issue in river basin management - summary
Uncertainty will be a key feature of the first set of river basin plans
Uncertainty will reduce over time, but will always be present and needs managing
Objective setting needs to take account of the confidence that a water body is truly worse than Good
For some pressures (eutrophication) a weight of evidence approach is needed to assess confidence of class
Need to be confident that there are biological impacts to justify actions