## Slide 1
Meeting the challenge of classification for the first river basin management plans
Richard Hemsworth, UK

## Slide 2
Produce first classifications in mid-2008 for inclusion in draft plans
….for 1,000s of water bodies
…subject to pressures not considered in pre-WFD classification schemes
The challenge

## Slide 3
For the draft plans, just 1 full year of monitoring data
Appropriate biological tools & sampling methods for hydromorphological pressures still limited
For the final plans, only 2 full years of monitoring data
Why is this a challenge?
Notes: Note: For hydrological impacts, if the year or years for which monitoring data area available are atypically wet years, impacts will not be identified.

## Slide 4
Limited suitable biological data for the first plan
…potential for classification results to give a misleadingly optimistic view
The risk

## Slide 5
Important to ensure classifications represent best current understanding of ecological status
For hydromorphological pressures, use all available data, including risk assessment results
Planned solution:

## Slide 6
..if we get another wet summer like 2007

## Slide 7
Risk analysis for hydrological pressures
River flow standards and lake level standards
- define supporting conditions for high, good, moderate and poor ecological status
- based on literature review; advice from independent experts; and public consultation

## Slide 8
- to estimate where the river flow and lake level standards are failed
….using national flow modelling tool, calibrated using data from river flow gauging stations

## Slide 9
Use of risk assessment results where no suitable biological data available | 
Class based on risk assessment results | Confidence of class
High | 
Good | 
Moderate | Medium confidence moderate or worse
Poor | 
Bad | 

## Slide 10
If the flow standards for poor/bad are failed, the river will dry for a period in most years

## Slide 12
Use of risk assessment results where no suitable biological data available | 
Class based on risk assessment results | Confidence of class
High | 
Good | 
Moderate | 
Poor | High confidence poor or worse
Bad | 

## Slide 13
Similarly…. risk analysis for morphological pressures
River, lake, transitional and coastal water morphological standards
- define supporting conditions for high, good, moderate and poor ecological status
- based on literature review; advice from independent experts; and public consultation

## Slide 14
Morphological classification takes account of:
Ecological sensitivity of different water body types
Ecological risk posed by different types of modification
All modifications to the water body

## Slide 15
Example where morphological classification = poor

## Slide 16
Confidence information is important to inform objective setting process

## Slide 17
Medium confidence or less
Significant risk investment in measures will be wasted
Apply extended deadline
Further monitoring & assessment to reduce uncertainty
High confidence
Low risk investment in measures will be wasted
Implement feasible and proportionate measures

## Slide 18
Risk assessment results can also be used to help confirm the cause of biological impacts

## Slide 19
Use of risk assessment results where suitable biological data is available |  | 
Class based on hydrological risk assessment results | Class based on relevant biological results | Confidence of class
High | High | 
Good | Good | 
Moderate | Moderate | High confidence moderate or worse
Poor | Poor | 
Bad | Bad | 

## Slide 20
Some conclusions
The use of risk assessment results can help meet the challenge of classification for the first plans
…and prevent the impact of certain pressures being under-represented
Where such results are used, providing appropriate information on confidence is important to inform objective setting