## Slide 1
Brussels, 6-7 March
Role of supporting elements in classification
The Netherlands
Marcel van den Berg / Centre for Water Management
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2
Not necessarily complex and difficult
Supporting element
Biology
Notes: <number>
<footer>
<header>
<date/time>
Was this the idea of the writers of the WFD? No difficulties, no discussion, straight forward classifications are possible.

## Slide 3
More realistic:
Supporting element
Biology
?
?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4
Solutions according Classification Guidance
Reducing mismatches by improving the relationship biology vs supporting elements
Reducing mismatches by setting new type specific standard
Notes: <number>
<footer>
<header>
<date/time>
Was this the idea of the writers of the WFD? No difficulties, no discussion, straight forward classifications are possible.

## Slide 5
Sources of mismatches in classifications
Both biology and chemical classification results contain errors related with sampling, analysis etc
Biological quality is a sum of a number of pressures and is never a 1:1 relationship
Biological quality can have alternative equilibriums in response to supporting elements
Biological quality can have time lack response to changing supporting elements
Notes: <number>
<footer>
<header>
<date/time>
Was this the idea of the writers of the WFD? No difficulties, no discussion, straight forward classifications are possible.

## Slide 6
Classification is related to setting standards
Mismatches are caused by error in relationships between Biology and Supporting elements and is ‘frustrated’ by lowest Quality Element determines classification
Conclusion
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Dutch approach in setting standards
LAKES: 90% certain that nutrients level keep or will result in Chlorophyll-a standards of Good or higher
RIVERS: 10% percentile of the nutrients values of sites that functions according definitions of Good Ecological Status of Macroinvertebrates
COAST/TRANSITIONAL: 90% certain that nutrient concentration results in phytoplankton GES
Based on yearly historical data bases
Information of other Quality Elments is not sufficiently or is also very dependent on other pressures than nutrients
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
Example: alternative equilibrium in very shallow lakes
GET voor TP
Used in the Netherlands
Notes: <number>
<footer>
<header>
<date/time>
Was this the idea of the writers of the WFD? No difficulties, no discussion, straight forward classifications are possible.

## Slide 9
Change supporting type specific standards to reduce mismatches in classification
Not really used in the Netherlands
Notes: <number>
<footer>
<header>
<date/time>
Was this the idea of the writers of the WFD? No difficulties, no discussion, straight forward classifications are possible.

## Slide 10: Phytoplankton vs nutrients; practical example
Coastal waters
Factor of exceeding the objective for nutrients
Phytoplankton EQR
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Practical example of relationship nutrient standard and (mis)classifications for coastal waters
BIOLOGY<GOOD
NUTRIENTS>=GOOD
BIOLOGY <GOOD &
NUTRIENTS <=GOOD
BIOLOGY >=GOOD
NUTRIENTS>=GOOD
BIOLOGY >=GOOD
NUTRIENTS<GOOD
The more precautionary a standard, the higher the
misclassification of BIO=good; NUT=moderate
Notes: <number>
<footer>
<header>
<date/time>
Toelichten dat checking procedure op type niveau weinig zinvol is: van te voren kun je aan de hand van hoe streng je de norm stelt bepaalt voorspellen hoeveel miscassificatie je krijgt. Hoe strenger de norm, dest te hoger het aandeel misclassificaties met bio=goed en nut=mod.

## Slide 12: The four combinations and their consequences
Nutrients good? Biology not? =Focus on management measures other than nutrient reduction
NUTRIENTS
BIOLOGY
GES
NO GES
GES
NO GES
BIO=NOT GOOD; NUT=NOT GOOD; Consider measures!
BIO=NOT GOOD; NUT=GOOD
Further analysis
BIO=GOOD; NUTRIENTS=
GOOD: No action required!
BIO=GOOD; NUT=NOT GOOD
Further analysis!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13
BIO
Classifications foreseen in 2009 for 2015 and their consequences for taking measures in RBMP for BIO=G and NUT=M
+
NUT
=
MES
BIO
+
NUT
=
MES
Further
analysis
+
=
MES
Measures
in RBMP
+
Measures
in first RBMP
BIO
+
NUT
=
MES
Further
analysis
+
=
MES
+
No Measures
in first RBMP
BIO
+
NUT
=
MES
Further
analysis
+
=
GES
+
No Measures
in first RBMP
Compliance check of individual water body on GES nutrients/supporting element
Notes: <number>
<footer>
<header>
<date/time>
Hier toelichten dat NL vindt dat in principe alle weergegeven opties zou moeten kunnen mogen gebruiken

## Slide 14
What is further analysis?
Carry out ‘’investigative monitoring’’ in Water Body concerned for further information
Further information or further analysis on present data can explain the mismatch in classification and can provide evidence for checking on normative definitions
Uncertainty analysis of being Moderate / Good may help to take the decision on taking measures
Notes: <number>
<footer>
<header>
<date/time>