## Slide 1: A proposal for reporting of WFD status of water bodies at European level
ECOSTAT Classification workshop, Brussels 6-7 March 2008
Jorge Rodriguez-Romero
Water Framework Directive Team
Unit D.2 – Water and Marine
DG Environment, European Commission

## Slide 2
Objective
Present a proposal for the reporting of the status of water bodies at European level for 2010
Contribution for WG D Reporting
This issue was left open in the 2010 reporting sheets endorsed by Water Directors in 2007

## Slide 3
The issue
WFD foresees reporting of the status class of water bodies
1 water body = 1 status class = 1 colour

## Slide 4
But intercalibration and the development of methods is not completed…
Member State 1:
Has a fully developed WFD compliant assessment system
Has intercalibrated two quality elements (as much as possible)
…and therefore good status is not fully comparable
Member State 2:
Has not yet developed WFD compliant assessment system
Has intercalibrated only one quality element
So this green is not the same as this green
MS1 MS2

## Slide 5
The initial proposal
Reporting maps at quality element level
Discarded as it results in patchy maps
Monitoring is carried out only in some water bodies and extrapolation is not necessarily done at quality element level
Macroinvertebrates
Phytobenthos
Fish

## Slide 6
The current proposal
1 water body = 1 status class = 1 colour
…but in addition provide information on what’s behind the status class
Example for rivers
Mi
Pb
Fi
Mp
PC
Hy
Macroinvertebrates
Phytobenthos
Macrophytes
Fish
Physico-chemical
Hydromorphology
This is not a proposal for presentation of the information. This is just to illustrate the type of information that according to this proposal, should be reported linked to the status class of a water body

## Slide 7
Possible values
Mi
Pb
Fi
Mp
Hy
PC
No information
High
Good
Moderate
Poor
Bad

## Slide 8
Example
Mi
Pb
Fi
Mp
PC
Hy
Mi
Pb
Fi
Mp
PC
Hy
Mi
Pb
Fi
Mp
PC
Hy
WB1: Information is available for Mi, Pb and PC. Status is determined by Mi and PC is consistent.
WB2: no monitoring information. Status has been extrapolated.
WB3: Information is available for Mi, Pb, Fi and PC. Status is determined by Fi.
Mi
Pb
Fi
Mp
PC
Hy
WB4: Information is available for Hy only. Status is derived by extrapolation + Hy

## Slide 9
Comments
Most of the information is already reported through the monitoring programmes, e.g. the quality elements that are monitored
This proposal would allow building impact maps based on information from various quality elements, although this would be done at aggregated level (i.e. RBD or sub-unit)

## Slide 10
Questions
Does this make sense?
Your comments are very welcome
We need to agree a concept for this reporting!
Thank you!