## Slide 1: Accounting for spatial variability in classifications
  Spatial variation
  Grouping
  Interventions
Notes: Starter slide.
Invite MS’s to make their technical interventions at the end of the presentation.
Ask MS’s to raise to intervene as we go if they are having difficulties understanding the presentation.

## Slide 2: Water bodies
Notes: Setting the scene – might get rid of this slide if necessary, could just talk this through without a slide. This slide will be used to help MS’s consider how they have treated water bodies. Have they decided that status within a water body is constant or have they considered spatial variation? Do they have sufficient monitoring in place to find these variations?).
Notes
The WFD does not describe how to designate water bodies. Even within the UK there are differences in approach (between Scotland and E&W). The method that each MS chose to delineate water bodies may be a reflection of regional population pressures and land use.
In England and Wales water bodies were designated using hydrological data only.
This means that we have many water bodies where there are known variations in ecological quality. This leaves us a problem – how do we account for the variations in a water body when we aggregate to water body level.

## Slide 3: Water bodies in England & Wales
Notes: Water bodies in the context of England and Wales – if necessary we could delete this one
Briefly display this map when talking about water body delineation.
Notes
For its size, E&W has a high number of water bodies compared to other Member States. The UK has a comparatively high population density that results in significant variations in environmental pressures within catchments.
Even with a high number of water bodies, there is significant variation in status within them. We know this because of our comprehensive monitoring programmes that have been in place for 20-30 years.

## Slide 4
Status: what do we want to know?
Overall status?
Worst status?
% or km less than good?
50%
Best status?
15% or 1.5km
Notes: What is the question: This slide will be used to provoke discussion and interventions on what answer we are looking for.
Notes
1. We might want only to report an overall status – aggregating monitoring station results to water body status.
2. We might want to report the status of the water body by using the results from the worst performing monitoring station.
3. We might set a spatial target, e.g. that if 15% of a water body is less than good status, we will classify using that component.
Which of three questions we are asking will depend upon what we want to do with the results. Do we want to identify every possible environmental problem in every water body? Do we want classification results to help prioritise programmes of measures?

## Slide 5
Grade a - Very Good
Grade b - Good
Grade c - Fairly Good
Grade d - Fair
Grade e - Poor
Grade f - Bad
U – Un-graded
GQA Biology Grade 06
River Lee
y
Diatoms
"
Fish
#
Macroinvertebrates
Z
Macrophytes
!
Phys chem
Element
Notes: Setting the local scene: Will improve this map. This catchment shows a strong variation in quality.
The water body we have chosen is at the bottom, it is over 30 km long. There is an obvious step change.
The upstream part of the catchment has a mix of agricultural and recreational uses, the water body then flows south through London and into the Thames Estuary. The population density increases dramatically as you travel downstream. The downstream end of the water body is heavily polluted from point source (STWs) and is heavily modified. It is also going to be a politically sensitive catchment, the 2012 London Olympic site will be built on the river bank.

## Slide 6: Options
Notes: Options We should make it clear that we are putting some options on the table for discussion. We could, if people are happy, say which one we are proposing – to stimulate a discussion.
The pictures will help illustrate the step-change in environment as you go down the water body.

## Slide 7: A – Identify a single representative station
Which one?
Notes: Option A – what class the water body would receive under option A.
Notes
The first option is simply to chose one assessment point.
You might want to chose the assessment point that is nearest to the downstream end, or the site with the most recent sample.

## Slide 8: B – Use all available information (average)
Options:
(i) Face value average
(ii) Account for spatial variations
Set an allowable zone of failure
Notes: Option B – what class the water body would receive under option B.
Notes
We should include 2 sub-options:
Simply mean or median of EQRs
A more advanced statistical appraisal of the water body based on known, or assumed, variability.

## Slide 9: (i) - Face value average
 | ASPT EQR
Site 1 | 0.97
Site 2 | 0.78
Site 3 | 0.62
Average | 0.79
MOD
Boundary | EQR
H/G | 0.97
G/M | 0.86
M/P | 0.75
P/B | 0.63
HIGH
MOD
BAD
Notes: Option B (i) – simple, face value average
Notes
A quick run through using real data (2000) shows how we would treat a large fluctuation in
status, simply by taking a face value mean.

## Slide 10: (ii) – Spatial variability
1 water body
Deviation zero – within section
3 sections
Within section variability = zero? not logical
Notes: Option B (ii) – a really close look at variability within a water body.
Notes
Lets think about how to take account of spatial variability within a water body and how might
take account of this when producing a classification. This example water body seems to have
three sections.
Can we assume that the ecological quality within each section remains constant? We could do,
and in the previous example we made this assumption.
But we know this isn’t logical.

## Slide 11
Spatial variability is 100% also not logical
Notes: Option B (ii) – a really close look at variability within a water body.
Notes
So, is it safe to assume there is 100 per cent variability within each section?
Probably not.

## Slide 12
Spatial variability is x per cent
Deviation?
Notes: Option B (ii) – a really close look at variability within a water body.
Notes
What we need is a known value of variability.

## Slide 13
What is the value of variance?
Mean total variance
‘Minimum’ total variance
Spatial variance lies in between
Acknowledgement: Robin Wyatt
Notes: Option B (ii) – a really close look at variability within a water body.
Notes
We can calculate spatial variation by looking at the variability within a dataset.
Richard – can you add an explanation.

## Slide 14: Using Viscous tool
Notes: Which option to use
Notes
The purpose of this slide is to make it clear that each MS will chose option A, B or C depending upon a number of factors:
- the method for delineating water bodies, was water quality taken into account
- WFD monitoring strategy; MS may have decided to use one assessment station per water body
- pre-WFD monitoring; evidence of variations in status will only be available if MSs have good historic monitoring programmes
What ever the decision, we recommend that MS consider how much of a water body is allowed to fail GES. The UK will use a 15 per cent or 1.5km threshold.

## Slide 15: Spatial allowance
How much of a water body is allowed to fail?
15% or 1.5km
Notes: Option B – what class the water body would receive under option B.
Notes
We should include 2 sub-options:
Simply mean or median of EQRs
A more advanced statistical appraisal of the water body based on known, or assumed, variability.

## Slide 16: C – Use worst class
Notes: Option C – what class the water body would receive under option C.
Notes
We should say why this option is only advisable if you want to make totally sure you do not
miss any zones of degradation. But the disadvantage is that you miss large zones where the
quality is actually very good.

## Slide 17: Which option to choose?
Water body designation
Monitoring strategy
Information about variability
Notes: Which option to use
Notes
The purpose of this slide is to make it clear that each MS will chose option A, B or C depending upon a number of factors:
- the method for delineating water bodies, was water quality taken into account
- WFD monitoring strategy; MS may have decided to use one assessment station per water body
- pre-WFD monitoring; evidence of variations in status will only be available if MSs have good historic monitoring programmes
What ever the decision, we recommend that MS consider how much of a water body is allowed to fail GES. The UK will use a 15 per cent or 1.5km threshold.

## Slide 18: Classifying TraC waters
1.5km2 or 15% of surface area of habitat must fail GES
Also used for number of samples within a habitat, e.g.
45 benthic invertebrate samples taken from soft sediment habitat, >7 failures (15%) = less than good.

## Slide 19: Classifying TraC waters
Available habitat
15% of habitat less than good
= 4 out of 25 samples

## Slide 20: Grouping
“Sufficient monitoring points within a selection of
the bodies in order to assess…diffuse pressures”
Notes: Grouping
Notes
Explain why grouping is needed and how we’ve interpreted the language of the WFD (page 54, 1.3.2, selection of monitoring sites).
We’ve used this to help us target our finite monitoring resources
Ask MS whether they have looked into grouping and whether they have succeeded.

## Slide 21: Grouping
Criteria
  Typology
  Risk Assessment
  Proximity
Results
  Group the overall status
  Confidence based on expert judgement
Notes: Grouping results. How we’ve grouped, at what level are we extrapolating status (EQR, QE, overall status) and how we are proposing to report.
Notes
.

## Slide 22: Example
No data
Data (for group)
Notes: Grouping results. Example.
Notes
.

## Slide 23: Conclusions and questions to pose
e.g.
Does this affect your MS?
Do you have any proposals to table?
Notes: Provoking discussion.
Notes
.