## Slide 1
Classification of ecological status for the 1st management plan
Brussels, March 6-7, 2008
Gisela Ofenböck
Federal Ministry of Agriculture, Forestry, Environment and Water Management
gisela.ofenboeck@lebensministerium.at

## Slide 2: Development of Assessment systems Biological Quality elements - Sensitivity to pressures
Biological Quality element | Hydro-morphol. pressures | Nutrients | Organic pollution | Acidifi-cation
Macro-invertebrates | ++ | ++ | +++ | ++
Phytobenthos Macrophytes | + | +++ | ++ | ++
Fish | +++ | + | + | +
Notes: When defining reference conditions it is necessary to take into account
that the assessment is done by analysing the deviation from the typespecific biological conditions
the time pressure due to the deadlines set in the WFD
we agreed to concentrate on best indicators
no need if it is already covered

## Slide 3: Macroinvertebrates
Biological Quality element | Hydro-morphol. pressures | Nutrients | Organic pollution | Acidifi-cation
Macro-invertebrates | ++ | ++ | +++ | ++
General Degradation
(Multi-metric Indices)
Nutrient Pollution and „Potamalisation“
Species Richness/Diversity (loss of habitats, species deficiency)Rhithralisation“
Saprobic Index
(typespecific)
Acidification Index
(Braukmann & Biss)
Notes: When defining reference conditions it is necessary to take into account
that the assessment is done by analysing the deviation from the typespecific biological conditions
the time pressure due to the deadlines set in the WFD
we agreed to concentrate on best indicators
no need if it is already covered

## Slide 4: Phytobenthos & Macrophytes
Biological Quality element | Hydro-morphol. pressures | Nutrients | Organic pollution | Acidifi-cation
Phytobenthos Macrophytes | + | +++ | ++ | ++
Phytobenthos
Saprobic Index
Phytobenthos
Reference Species Index
Phytobenthos
Trophic
Index
Macrophyte Index
Notes: When defining reference conditions it is necessary to take into account
that the assessment is done by analysing the deviation from the typespecific biological conditions
the time pressure due to the deadlines set in the WFD
we agreed to concentrate on best indicators
no need if it is already covered

## Slide 5: Fish
Biological Quality element | Hydro-morphol. pressures | Nutrients | Organic pollution | Acidifi-cation
Fish | +++ | + | + | +
Fish Index
Austria
(FIA)
?
EFI +
?
Notes: When defining reference conditions it is necessary to take into account
that the assessment is done by analysing the deviation from the typespecific biological conditions
the time pressure due to the deadlines set in the WFD
we agreed to concentrate on best indicators
no need if it is already covered

## Slide 6: Pressure & Impact Analysis 2004: Rivers > 100 km2
Results Risk Analysis
60%
24%
16%

## Slide 7: Design of monitoring system
Surveillance Monitoring:
Ü1: sites with high relevance
Ü3: additional sites
Ü2: reference sites
Operational Monitoring:
WB with risk (chemical / hydromorphological
assessement of measures
international obligations
overlaps
selection of sites integrated in international networks )TNMN)
Investigative Monitoring
regulated by ministry (BMLFUW)
regulated by provinces

## Slide 8: Surveillance Monitoring
3 different types of monitoring sites:
  Ü1: sites with high relevance
  Ü2: reference sites
  Ü3: additional sites
permanent measurement of all parameters
criteria for selection in the legal regulation GZÜV
76 monitoring sites
 | Ü1 | Ü2 | Ü3
rivers | 31 | 5 | 40

## Slide 9: Operational Monitoring
surface waters > 100 km² monitoring 2007-2008
surface waters 10 – 100 km² start 2010
Selection of relevant waterbodies for 2007-2008:
         Based on Risk Analysis Art 5 WFD
         Includes all waterbodies > 100 km²
        - at risk(3) or
        - possibly at risk (2)
Establish status of those water bodies identified as being „at risk“

## Slide 10: Operational Monitoring selection of relevant parameters
based on risk analysis
„most indicative quality element“
    not all quality elements – only most sensitive
    depending on pressure
    combined pressures – combined quality elements
    worst case principle

## Slide 11: Operational Monitoring Most indicative quality element
Chemical Pressures | General physico-chemical Para-meters | Pollu-tants | Phyto-benthos | Makro-phytes | Macro-inverte-brates | Fish
Nutrients | x |  | x | (x) | (x) | 
oxygenation conditions | x |  | (x) |  | x | (x)
Temperature | x |  |  |  | (x) | x
Salinity | x |  | (x) |  | (x) | x
Acidification | x |  | (x) | x | x | (x)
Pollutants | x | x |  |  |  | 

## Slide 12: Operational Monitoring Most indicative quality element
Hydromorphological pressures | General physico-chemical Para-meters | Pollu-tants | Phyto-benthos | Makro-phytes | Macro-inverte-brates | Fish
morphological alterations |  |  |  | (x) | (x) | x
stream bed modifications |  |  |  |  | x | (x)
residual flow |  |  |  | (x) | (x) | x
hydro peaking |  |  |  | (x) | (x) | x
impoundment |  |  |  | (x) | x | (x)
interruptions of continuum |  |  |  |  | (x) | x

## Slide 13: Operational Monitoring Chemical Pollution WB > 100 km²
Each waterbody „at risk“ or „possible at risk“ needs at least one monitoring site
      Excemption: consecutive waterbodies with diffuse pollution)
      Use of Existing data (2005 – 2007)
      198 waterbodies at risk or possibly at risk (72 specific chemical pollutants (origin mainly point sources, incl. Ammonium, Nitrit)
      Sampling site at end of water body
Quality elements: Physico-chemical parameters, relevant pollutants, Macroinvertebrates, Phytobenthos

## Slide 14: Operational Monitoring hydromorphological pressures
Many water bodies at risk but limited number of monitoring sites  representative monitoring necessary
Groups of waterbodies
  typology: similar natural conditions with regard to the relevant BQE  fish typology
  pressures and combinations of pressures:
    28 combinations out of 32 possible combinations
    5 dominant combinations: cover 60% of water bodies at risk

## Slide 15
Ca. 600 water bodies at risk – ca. 30% monitored, ca. 400 sites
Quality elements: Fish, (Macroinvertebrates)
Operational Monitoring hydromorphological risk

## Slide 16: Classification of waterbodies (hydromorphological pressures)
x % within a water body
If there are different status classes within a water body – how much deviation from good status is acceptable? Still under discussion!
Maximum length of x meters

## Slide 17
Status of Water bodies
Problem: few monitoring results available, but classification of all water bodies necessary
GROUPING PROCEDURE for
  biological qualtity elements
  physico-chemical elements from diffuse sources
Two steps
  Simple grouping procedure
  Expert grouping procedure

## Slide 18: Simple grouping procedure
Criteria:
impoundment > 1000 m
no flow (river at least temporally dry)
not enough water for fish migration
hydropeaking > 1:5
bad morphology (class 4-5) dominant (i.e. form more than 50% of water body length)
several migration barriers (Potamal and transition to Hyporhitral)
Is it possible to classify the status of the water body as bad without grouping – due to extreme values for the pressures?
YES
NO
criteria
bad status
high confidence

## Slide 19: Simple grouping procedure
Is it possible to classify the status of the water body as bad without grouping – due to extreme values for the pressures?
NO
Same result for all respresentative WBs of the group?
Risk due to chemical pollution from diffuse sources
Risk due to
hydromorphology
Result from the downstream site is transferred to water bodies located upstream
high confidence
NO
YES

## Slide 20: Simple grouping procedure
Same result for all respresentative WBs of the group?
Risk due to
hydromorphology
NO
YES
average EQR=
result for all WBs of the group
high
confidence
average EQR=
result for all WBs of the group
with specification of confdence: high or low
confidence level:
high: distance between average and class boundary 2/3 is more than ½ class witdth
low: distance between average and class boundary 2/3 is less than ½ class witdth

## Slide 21: No monitoring data available (e.g. small rivers)
Criteria:
impoundment > 1000 m
no flow (river at least temporally dry)
not enough water for fish migration
hydropeaking > 1:5
bad morphology (class 4-5) dominant (i.e. form more than 50% of water body length)
several migration barriers (Potamal and transition to Hyporhitral)
Is it possible to classify the status of the water body as bad without grouping – due to extreme values for the pressures?
YES
NO
criteria
bad status
high confidence
Moderate status
(or worse)
Low confidence
All water bodies at risk or possibly at risk

## Slide 22: Expert grouping procedure

## Slide 23: Status classification
Status category = confidence level of achievement / failure of quality objective | Confidence level of correct assessment of status class | Description | Illustration in map
Very high confidence (assessment with sampling data) | Very high | Assessment with data from sampling sites. Very high confidence results from: adequate sampling strategy QA – measures plausibility check of results | 
High confidence | medium | Assessment using conclusions. High confidence results from: distance from boundary good/moderate statistical confidence | 
Low confidence | low | Assessment using conclusions. High confidence results from: statistical uncertainty low confidence due to use of risk criteria | 

## Slide 24: Thank you for your attention!