## Slide 1: Future climate scenarios for phosphorus and nitrogen dynamics in the Gulf of Riga
Bärbel Müller-Karulis, Latvian Institute of Aquatic Ecology
Juris Aigars, Latvian Institute of Aquatic Ecology
In colaboration with Juris Seņņikovs, Laboratory for Mathematical Modelling of Environmental and Technological Processes, Faculty of Physics and Mathematics, University of Latvia
Latvian Institute
of Aquatic Ecology

## Slide 2: Gulf of Riga characteristics
Semi-enclosed basin
Connected to Eastern Gotland basin surface waters
Salinity 5.5 – 6.2 PSU
Shallow: average depth 22 m, maximum 56 m
no permament halocline, seasonal thermocline, monomictic circulation
High freshwater and riverine nutrient input
Regular monitoring since 1973
Response to climate change
?

## Slide 3: Mean temperature (period 1973-2008)

## Slide 4: Mean oxygen (period 1973-2008)

## Slide 5: Model setup
Biogeochemical model
  phytoplankton, zooplankton and nutrients
  NPZD Box model based on Savchuk 2002
  2 boxes (pelagic, demersal) + sediments
  3 phytoplankton groups
  Zooplankton
  NO3, NH4, PO4, O2
  Calibrated to 28-year observation series
Physical model (1D)
  vertical temperature distribution in the GoR
  General Ocean Turbulence Model (GOTM)
  Coefficients of second order model: Cheng (2002)
  Dynamic equation (k-ε style) for TKE
  Dynamic dissipation rate equation
Temperature change
Ecosystem response

## Slide 6: Climate change scenario
Climate data from PRUDENCE. Control: 1961-1990, Scenario A2: 2070-2100
Extra downscaling of RCM data (bias correction via histogram equalisation):
relative humidity (used variable td2m)
air temperature (used variable t2m)
Original RCM data:
sea level pressure (used variable MSLP)
cloudiness (used variable clcov)
wind speed (used variable w10m)
wind direction (used variable w10dir)
Calculations made for Gulf of Riga (50 m), 30 year period, daily output data – water temperature

## Slide 7
Physical model results – I (mean temperature distribution over depth)
T increase by 1,5 (bottom) to 3 (surface) degrees
Surface T increase close to air T increase

## Slide 8
Physical model results – II (mean daily pycnocline depth and its variation)
Pycnocline develops earlier...
... stratification lasts longer

## Slide 9
Physical model results – III (mean time-depth plots of temperature)
Contemporary climate
Climate change scenario A2

## Slide 10: Vertical water exchange
decreased vertical water exchange

## Slide 11: Demersal oxygen – GR mean

## Slide 12: Species succession
earlier and more vigorous spring bloom

## Slide 13: Species succession
larger biomass of summer species

## Slide 14: Species succession
more cyanobacteria

## Slide 15: Pelagic nutrients
larger winter pool
earlier depletion

## Slide 16: Demersal nutrients
larger demersal nutrient concentrations in summer

## Slide 17: Vertical nutrient flux
increased demersal concentrations compensate stratification effect

## Slide 18: Nutrient regeneration
Pronounced increase in nutrient recycling!

## Slide 19: Denitrification

## Slide 20: Nitrate uptake/release (oxygen control)

## Slide 21: Ammonium versus nitraterelease
Chart: NH4 µmol m-²d-¹
| 776.25946499999998 | 542.73430999999994 | 921.39864000000011 | 1046.1860799999999 | 1286.4027499999997 | 1935.9082100000003 | 2642.8640799999998 | 1913.6393975000001 | 2316.4673699999994 | 2492.29288 | 2191.9349999999999 | 1940.9866666666665 | 8.8515000000000086 | 190.47333333333336 | 357.346 | 444.03425000000004 | 482.03250000000003 | 382.37799999999999 | 288.42900000000003 | 464.54866666666663 | 288.78375
 | -266.3521 | -305.6395 | -511.3798 | -374.3094 | -389.3045 | -575.7086 | -582.382 | -482.2333 | -684.647 | -611.382 | -618.3836 | -504.8607 | 190.89 | 25.35 | 7.0975 | -19.3019 | -93.3091 | 85.8414 | 122.4642 | 1.161 | 28.8145
 | -187.5932 | -240.8302 | -95.1542 | -232.1313 | -216.7458 | -200.4633 | -163.1584 | -178.7175 | -219.9196 | -164.1124 | -114.726 | -111.455
 | 121.3275 | 115.8567 | 207.0475 | 224.3032 | 233.0679 | 286.9367 | 170.965 | 276.9684 | 252.8357

## Slide 22: Mean nitrate (period 1973-2008)

## Slide 23: Conclusions
Increase in phytoplankton growth and primary productivity caused by increased nutrient regeneration
Slightly increased winter nutrient concentrations
Earlier spring bloom (earlier stratification, no ice cover)
Larger summer phytoplankton biomass, more cyanobacteria because of more intensive nutrient regeneration
Lower demersal oxygen concentration caused by more stable and longer stratification
Denitrification – open question for future research